## Slide 1
Update on SAGE III/ISS temperature and pressure research products
Michael Pitts1, Robert Manion2, Robert Damadeo1, David Flittner1, Mary Cate McKee3
1NASA Langley Research Center, Hampton, Virginia
2Adnet Systems, Inc., Hampton, Virginia
3Analytical Mechanics Associates, Hampton, Virginia
14 August 2025

## Slide 2: Outline
Brief overview of T/p retrieval algorithm
Assessment of forward model
Correlative comparisons
Potential sources of uncertainty
Summary and ongoing work

## Slide 3: Strategy for Temperature/Pressure Retrievals
Iterative approach required due to non-linear nature of problem
Uses non-linear least squares fitting routine (Levenberg-Marquardt)
  Simultaneously fits measured A-band spectra from all 14 channels and 90 tangent altitudes
    Includes O2 absorption, Rayleigh scattering, aerosol extinction, and O3 absorption components, plus wavelength and PSF adjustments
    Implemented at the SCF
  Solves for successive adjustments to trial T,p profiles by minimizing residuals between measured and modeled absorption
  Includes non-rigid hydrostatic constraint
A-band contains ~290 individual absorption lines with the distinctive R-branch and P-branch structure. Broad features are still visible at SAGE III resolution (red line)
14 Channels at ~ 1-nm intervals
FWHM ~ 1.4 nm
SNR ~ 1500

## Slide 4: Forward Model Elements
Forward model simulates SAGE III/ISS LOS transmission measurements in 14 O2 A-band channels using LBL radiative transfer calculations
Inputs:
  Initial guess T/p profiles
  Pathlength matrix
  O2 Spectroscopic parameters (HITRAN 2020)
  Initial guess aerosol (linear fit: slope + intercept)
  Initial guess ozone (cross sections + ozone number density)
  Initial wavelength map
  Initial PSF widths
Outputs
  LOS transmission (O2 + Rayleigh + aerosol + O3)

## Slide 5: Retrieved Wavelength and PSF Width Adjustments to Best fit Measured Spectra
Drift of wavelength shift with time may be related to general warming of instrument/ spectrometer as thermal systems have aged
Systematic differences between SR & SS may be related to Doppler shift from spacecraft motion
Only slight adjustment to PSF widths
Instrument PSF
Prelaunch NIST
Model with Gaussians
SS change
2018-2024
SR change
2018-2024

## Slide 6: Forward Model Fitting LOS Total (O2 + Rayleigh + aerosol + O3) Extinction Spectra

## Slide 7: Aerosol & O3 Component Fitting
“Measured” aerosol and O3 components interpolated from aerosol channels and AO3 ozone product
Combined retrieved aerosol + O3 components agree well with “Measured” values with slight slope difference
Retrieval has difficulty separating aerosol & O3 contributions
Possible cross talk between aerosol/O3 fitting and O2-Rayleigh fitting
Aerosol/O3 Component Profiles
SR Event January 2018
Channel 4 ~ 762 nm
Aerosol/O3 Component Spectra
25 km
Aerosol
O3

## Slide 8: Correlative Comparisons MERRA-2 & Aura MLS (2024)

## Slide 9: Correlative Comparisons SABER & ACE (2024)

## Slide 10: Correlative Comparisons (2024) ALL
Preliminary Assessment
Systematic warm bias 20-40 km & upper mesosphere
Too cold at tropopause and stratopause

## Slide 11: O2 A-band Spectroscopy Uncertainty
Recent lab measurements differ in magnitude and spectral shape from previous HITRAN compilations
Modeled line shape
  Currently using standard Voigt profile (VP)
  More advanced line shapes are likely more accurate, e.g.
    Speed dependent Voigt profile (SDVP)
    Speed dependent Nelkin-Ghatak profile (SDNGP)
Line intensities
E. M. Adkins et al., An accurate determination of O2 A-band line intensities through experiment and theory, JQSRT, 2025.
D.A. Long et al., The effects of advanced spectral line shapes on carbon dioxide retrievals, JQSRT, 2021.

## Slide 12: Summary and Ongoing Work
Retrieval algorithm including wavelength and PSF width adjustments implemented at SCF
  Wavelength adjustments of ~0.05 nm for SS and ~0.09 for SR with systematic drift over mission possibly due instrument/spectrometer warming as thermal systems age
  PSF widths slightly larger than baseline
Forward model assessment
  Modeled LOS extinction spectra accurately fit measured spectra (typically < few percent except in weak channels at high altitudes)
  Combined aerosol + ozone components match well with “measured” values
Correlative comparisons
  SAGE III/ISS temperature profiles capture fundamental features of atmospheric thermal structure, but warm bias in stratosphere (20-40 km) and above ~ 70 km
Ongoing Work:
  Continue refining forward model parameters (e.g., spectroscopy and instrument response)
  Expand correlative comparisons to include full mission time period & additional instruments (e.g. ground-based lidars)
  T/p research products anticipated to be included in final data product release